## Slide 1: Machine learning for underground gas storage with cushion CO2 using data from reservoir simulation
Johan Olav Helland, Helmer André Friis, Mohsen Assadi, Stanislaw Nagy
University of Stavanger
AGH University of Krakow

## Slide 2: Underground natural gas storage (UNGS)
Temporary storage of natural gas (e.g., methane CH4) in salt caverns, aquifers or depleted reservoirs, that is produced upon demand and/or to maintain a steady energy supply
  Seasonal injection/production cycles
The use of a cushion gas contributes with pressure support and limits the extent of capillary trapping of the natural gas
Advantages with CO2 as cushioned gas:
  The compressible property improves the storage capacity and aids the CH4 production
  A possible solution for permanent CO2 storage
Challenges with CO2:
  Mixing of CO2 and CH4 can lead to CO2 production
  CH4 is less viscous than CO2 (viscous fingering)
Shoushtari et al., (2023) Journal of Energy Storage 67, 107596

## Slide 3: Objectives
Reservoir simulations of UNGS with cushioned CO2 to gain insights and generate data for data-driven methods:
  One-well CH4 injection-production cycle:
    Conditions for maximal CH4 production and minimal CO2 production
  Seasonal CH4 injection-production cycles with continuous CO2 injection using different wells:
    Investigate behaviour with respect to well placement and CO2 injection rate.
Develop artificial neural network (ANN) models that describe the results and allows for fast estimation for different parameter combinations

## Slide 4: Reservoir model
Simulations of two-component flow of CH4 & CO2 with gravity in 2D idealized reservoirs using the MRST simulator (Compositional module)
Rate-controlled, vertical wells with radius 10 cm
No-flow boundary conditions
Permeability anisotropy, .
Initially, the reservoir is filled with CO2 and the pressure is 6 MPa
Size of grid blocks: m3
CH4
CO2
m

## Slide 5: One-well injection-production cycle
The well is placed on left side, 3 m from top boundary
Injection and production rates of 0.015 m3/s
Systematic variation of reservoir height (), temperature (), porosity (), horizontal permeability (), injection time (), using 1200 simulations

## Slide 6: One-well injection-production cycle
Decline of CH4 mole fraction in the well during production
How long can we produce CH4 before the CO2 mole fraction in the well exceeds 1%?
90 days
240 days

## Slide 7: One-well injection-production cycle
A simulation with midrange parameters compared with new simulations where one parameter at a time was replaced by its maximum and minimum value
The results show that and have largest impact on well-block mole fraction over time:

## Slide 8: ANN model for «optimal» production time
Developed using TensorFlow in a Python environment
Input parameters: , , , ,
Output: Production time until CO2 mole fraction in well exceeds 1%
Data from the 1200 simulations are split into training (87.5%), validation (6.25%), and test (6.25%) sets.
ANN model specifics:
  Adam optimizer
  Mean squared error as metric & loss function
  Activation function: ReLu
  Two hidden layers with 42 and 15 neurons
  Trained for 200 epochs

## Slide 9: Multiple storage cycles & wells
Same reservoir as before, with m, K, , mD.
3 wells:
- CO2 injection well: 37 m below the top seal at left boundary
- CH4 injection well: 3 m below the top seal at a distance from left boundary
- Production well: 3 m below the top seal at right boundary

## Slide 10: Multiple storage cycles & wells
Schedule of processes:
  360 days of CH4 injection with a rate of 0.025 m3/s in the CO2-filled reservoir.
  180 days of gravity segregation with all wells closed.
  3 cycles of CH4 injection (180 days) and withdrawal (180 days) with rate of 0.015 m3/s, while CO2 injection occurs from the third well with a rate of .
Investigate behaviour for different well positions () and CO2 injection rate ()

## Slide 11: Multiple storage cycles & wells
30 days
Initial CH4 injection (30 days)
End of 1st seasonal production (900 days)
End of initial CH4 injection (360 days)
End of 3rd seasonal production (1620 days)
Increased CH4/CO2 mixing zone at the flanks and below production well
m, m3/s

## Slide 12: Multiple storage cycles & wells
Impact of CO2 injection rate () for constant well position ()
Well-block pressure increases with seasonal cycle and CO2 injection rate
Increased injection rate leads to slightly lower CO2 production in the first seasonal cycle but higher CO2 production in later cycles

## Slide 13: Multiple storage cycles & wells
Impact of well position () at constant CO2 injection rate ()
Impact of on the pressure in production well is insignificant.
Smaller spacing between CH4 injection & production wells leads to the least CO2 production.

## Slide 14: ANN model for well-block mole frac. & pressure
Input: , , and seasonal cycle number
Output: CO2 mole fraction & pressure in production well after each season
ANN performance on the training data:
ANN model specifics:
  Adam optimizer
  Mean squared error as metric & loss function
  Activation function: ReLu
  Two hidden layers with 27 and 15 neurons
  Trained for 600 epochs

## Slide 15: ANN model for well-block mole frac. & pressure
ANN performance on new reservoir simulations with other values of & :

## Slide 16: Conclusions
Reservoir simulation and ANN models were used to explore seasonal injection & withdrawal cycles in UNGS with cushion CO2.
To avoid CO2 production, it is paramount to have a significant amount of CH4 present in the reservoir before seasonal cycles begin.
Decreased spacing between CH4 injection & production wells leads to the least CO2 production during seasonal cycles. Hence, the optimal setting is to use the same well for production and injection.
Continuous CO2 injection during UNGS has a marginal positive effect in the first cycle, while later cycles exhibit increased CO2 production and undesired pressure build-up that worsen with increased CO2 injection rate.
Trained ANN models describe the behavior of well-block mole fraction and pressure over time during UNGS. Hence, ANN models are useful tools to optimize UNGS operation with respect to increased gas deliverability and minimized CO2 production.

## Slide 17: Acknowledgments
This research was funded by EEA and Norway Grants, operated by The National Center for Research and Development, grant number NOR/POLNORCCS/AGaStor/0008/2019-00.