## Slide 1: Finite Element Analysis and Simulation of Lag Screw Insertion by Robotic Arm for Basicervical Hip Fractures
Filippos Vlontakis1, Pantelis Nikolakopoulos1, Panagiotis Koustoumpardis1, Antonios Kouzelis2, Antonis Sakellarios1
1University of Patras, Greece, 2General University Hospital of Patras, Greece
Olympiad of Engineering Science 2025, University of Stavanger, Norway
10-14 June 2025

## Slide 2
Presentation Contents
Introduction to hip fractures
Surgical Technique for Basicervical Fractures
Methodology
Results

## Slide 3: Introduction
Femoral
Head
Neck
Intertrochanteric area
Basicervical Fractures
Proximal Femur Fractures
By 2050, estimated occurrence rate of 4.5 million incidents/year [Cooper et al., 2011]
Great economic burden to healthcare systems (12.000$ average cost per incident in the US in 2022 [Ferris et al., 2022])
Result of impact trauma and/or pathological conditions (osteoporosis)
3/17
Basicervical Femur Fractures
  Relatively rare subtype of proximal femur fractures (1.8 – 7.6% of total incidences [Dekhne et al., 2021])
  Unstable fractures, weightbearing promotes development of shear stress along fracture line
  ~50% of cases treated with osteosynthesis
  During surgical operation, reported relative rotation of the femoral head with respect to stem

## Slide 4: Surgical Procedure
Fracture reduction
Closed reduction using fracture table
Displaced fracture
Restoration of anatomical morphology of proximal femur prior to commencement
4/17

## Slide 5: Surgical Procedure
Implant insertion
Insertion Handle
Intramedullary nail
Intramedullary canal reaming and nail insertion (not modelled)
Drilling and lag screw insertion
Aiming Arm
Lag Screw
As lag screw gains purchase in femoral neck, compression nut is used to generate compression force along the fracture surface
5/17

## Slide 6: Methodology Overview
Development of FE model to investigate biomechanical behavior of system during lag screw insertion
Simulation of robotic arm control loop for semi-automated surgical procedure
QCT
Geometry Reconstruction
CAD model
Discretization
Constitutive
modelling of bone
2. FE model
Relative motion
Stress
Strain
3. Transition to control
6/17
Position Control
Force Control
End-Effector Force
Config
1. Pre-Processing
4. Manipulator control

## Slide 7: 1. Preprocessing
Segmented QCT proximal femur scans, from osteoporotic patient (no fracture)
CAD geometry, introduction of virtual fracture line
Virtual implant insertion to position of interest
Meshing using 10-node tetrahedral elements
(360k elements, 550k nodes)
Calibration phase
Radiological bone to ash density
Ash density to Young’s modulus
Inhomogeneous distribution of bone material properties
Axial View
Coronal View
7/17

## Slide 8: 2. Finite Element Modelling
Static-Dynamic Friction
-
𝝁(𝒗)= 𝝁_𝒅+(𝝁_𝒔 - 𝝁_𝒅)𝒆^(−𝒄𝒗)
𝝁_𝒅=𝟎.𝟑𝟕, 𝝁_𝒔=𝟎.𝟒𝟏, 𝒄=𝟏𝟎
From experimental data [Grant et al., 2007]
Static-Dynamic Friction
Static Friction
From experimental data [Eberle et al., 2010]
𝝁_𝒔=𝟎.𝟒𝟕
Static Friction
Boundary Conditions
Contact Definition
3 load steps
Tractive force development
Rotational acceleration of lag screw
Stabilization
(1)
(2)
(3)
8/17

## Slide 9: 3. Transition to control of robotic arm
Estimation of equivalent elastic constant due to end effector interaction with environment
9/17

## Slide 10: 4. Robotic Arm Control Scheme
Multibody Dynamics model of the arm
Position Control (1 DoF)
Force Control (5 DoF)
Centralized control scheme in cartesian space
(6 DoF of end-effector)
10/17

## Slide 11: Results – Friction at Bone Implant Interface
[0 - 0.2sec]
No relative motion at the interface
[0.2 – 0.3 sec]
Partial Sliding until max static friction
[0.3 – 1.3 sec]
Full sliding at the interface
Tractive Force Development
Rotational Acceleration of Lag Screw
Steady Rotational Speed Rotation of Lag Screw
11/17

## Slide 12: Results – Contact at the Fracture Area
Contact Pressure Stabilization
Relative Sliding Stop
Maximum Relative Displacement
12/17

## Slide 13: Results – Robotic Arm Control System Errors
Tractive Force Development
Rotational Acceleration of Lag Screw
Steady Rotational Speed Rotation of Lag Screw
Maximum absolute force error in x-axis
13/17

## Slide 14: Conclusions
Finite Element Model
Sliding at fracture governed by frictional forces at the bone-implant interface
Novel surgical method application results in very small femoral head rotation relative to the stem, improving post-surgical fracture reduction
Robotic Arm Simulation
Position control system showed very good response with minimal errors
Force control system introduced errors (-7.5% to 5%), at critical points for the procedure
14/17

## Slide 15: Future Work
Generalization of findings
  Use of more CT scans (varying degrees of osteoporosis)
  Vary the fracture patterns
Model validation
Work with clinicians to determine realistic constraints for the movement of the robotic arm
Coupling Simulink and ANSYS models
15/17

## Slide 16: Thank you!

## Slide 17: Literature
Cooper, C., Cole, Z.A., Holroyd, C.R. et al. Secular trends in the incidence of hip and other osteoporotic fractures. Osteoporos Int 22, 1277–1288 (2011). https://doi.org/10.1007/s00198-011-1601-6.
Ferris, H., Brent, L. & Sorensen, J. Cost of hospitalisation for hip fracture-findings from the Irish hip fracture database. Osteoporos Int 33, 1057–1065 (2022). https://doi.org/10.1007/s00198-021-06294-7
Dekhne MS, Thomas HM, Haider T, et al. Treatment and outcomes of basicervical femoral neck fractures: A systematic review. Journal of Orthopaedic Surgery. 2021;29(1). https://doi.org/10.1177/23094990211003344
Kijima H et al. Characteristics and Treatment Strategies for Basicervical and Transcervical Shear Fractures of the Femoral Neck. Journal of Clinical Medicine. 2023; 12(22):7024. https://doi.org/10.3390/jcm12227024
Young-Kyun Lee et al., Risk factors of fixation failure in basicervical femoral neck fracture: Which device is optimal for fixation?, Injury. 2018;49(3). https://doi.org/10.1016/j.injury.2018.02.009
Massoud, E.I.E. Fixation of basicervical and related fractures. International Orthopaedics (SICOT) 34, 577–582 (2010). https://doi.org/10.1007/s00264-009-0814-1
Konya MN, Verim Ö., Numerical Optimization of the Position in Femoral Head of Proximal Locking Screws of Proximal Femoral Nail System; Biomechanical Study. Balkan Med J. 2017 Sep 29;34(5):425-431. https://doi.org/10.4274/balkanmedj.2016.0732.
Stryker Corporation, “Gamma3 Trochanteric Nail 170 & 180, Operative Technique.”
J.A. Grant et al., Artificial composite bone as a model of human trabecular bone: The implant–bone interface, Journal of Biomechanics, 2007;40(5) https://doi.org/10.1016/j.jbiomech.2006.04.007.
Eberle S et al., A Biomechanical Evaluation of Orthopaedic Implants for Hip Fractures by Finite Element Analysis and In-Vitro Tests. Proceedings of the Institution of Mechanical Engineers, Part H: Journal of Engineering in Medicine. 2010;224(10):1141-1152. https://doi.org/10.1243/09544119JEIM799
J. Y. S. Luh, M. W. Walker, and R. P. C. Paul, “On-Line Computational Scheme for Mechanical Manipulators,” J Dyn Syst Meas Control, vol. 102, no. 2, pp. 69–76, Jun. 1980, https://doi.org/10.1115/1.3149599.
25/25