## Slide 1: Numerical modelling of H2 deflagrations in EXSIM
Jamie Thompson, DNV Stockport
Bjørn Erling Vembe, DNV Stavanger

## Slide 2: Agenda
Introducing EXSIM
  What is EXSIM?
  What can you do with it?
Code validation
  Focus on hydrogen
Summary

## Slide 3: Introducing EXSIM

## Slide 4: Overview
What is EXSIM?
  Advanced CFD-based simulator for calculation of gas explosion consequences in complex geometries
A bit of History…
  Originally developed in 1989 by Professor Bjørn Hjertager at Tel-Tek/Telemark University (Norway)
  Further developed as joint IP with Shell
  Subsequently used for more than 20 years as Shell’s primary explosion simulator for complex geometries
  IP acquired by ComputIT (now DNV) in 2014, becoming commercially available as integrated part of KFX suite in 2015

## Slide 5: Capabilities
Accurate prediction of consequences of gas explosions in complex geometries
  Both offshore and onshore
  Range of fuel types (including hydrogen)
Overpressure predictions:
  As a function of space and time
  Averaged over surfaces (e.g. loading on walls)
Dynamic pressure predictions:
  Drag loading on piping, structures etc.
Effects of wall failure, opening of blast panels etc.

## Slide 6: Validation (EXSIM 7.0)

## Slide 7: Model Validation
EXSIM is actively being developed and validated
Recently completed a multi-year JIP focused on improving predictive capabilities for hydrogen explosions
  Improved quasi-laminar combustion model
  Revision of underlying PDR/k-ε formulation
  Updated meshing guidelines
The following slides summarise the results of recent validation work for hydrogen explosions in both highly and lightly congested environments
  Note: Presented results obtained from upcoming release, EXSIM 7.0

## Slide 8: Hydrogen deflagration modelling validation
SATO MEDIUM SCALE H2 TEST
Hysea homogeneous H2 TESTS
Shell h2 refuelling station mock-up

## Slide 9: Sato medium scale tests
Test performed by Sato et al. in 2006
Fuel-air mixture contained in ‘empty’ tent
  Dimensions: 4.3 m x 4.3 m x 2 m
  Some limited framing/fixtures
Rig engulfed in fuel-air mixture
  Ignited centrally (ground level)
Test was well instrumented
  Ionisation pins for flame position measurement
  Pressure transducers at distances of 2 – 41 m from ignition point
Photos: Sato et al. (2006)

## Slide 10: Simulation setup
No geometry required
  Framing not considered significant
  (Insufficient detail anyway…)
Mesh:
  Core region: 0.25 m
  Monitor region: 0.50 m
  Expansion factor: 1.05
Fuel:
  Hydrogen
  Equivalence ratio: 1.02

## Slide 11: Sato medium scale: results
Significant underprediction observed for pre-JIP version
  No predictions within a factor of 2 of experimental values
  Likely to be attributable to QL model for H2
Predictions for updated model generally in excellent agreement with experimental data
  Some underprediction in near-field, however
  Predicted within factor of 2 of experimental value 100% of the time
Pre-JIP
Updated

## Slide 12: Sato medium scale: results
Significant underprediction observed for pre-JIP version
  No predictions within a factor of 2 of experimental values
  Likely to be attributable to QL model for H2
Predictions for updated model generally in excellent agreement with experimental data
  Some underprediction in near-field, however
  Predicted within factor of 2 of experimental value 100% of the time
Pre-JIP
Updated

## Slide 13: HySEA homogeneous tests
HySEA project ran from 2016-2019
  Aim was to ‘provide pre-normative research on vented deflagrations in enclosures and containers for hydrogen energy applications’
Model validation tests performed by Gexcon
  Two tests assessed
  Both previously used for ‘blind predictions’ exercise
Test rig comprised 20 ft ISO-container
  Doors open, with steel framing at floor level
  Test A: Frame only (‘empty’)
  Test B: bottle basket with 20 50-litre cylinders included
Container filled with lean H2-air mixture
  Equivalence ratio: 0.42
  Ignited at rear face of container
Images: Skjold et al. (2017)

## Slide 14: Simulation setup
Fuel:
  Hydrogen
  Equivalence ratio: 0.42
Mesh:
  Core region: 0.16 m
  Monitor region: 0.5 m
  Expansion factor: 1.05

## Slide 15: HySEA homogeneous: results
Clear tendency to overpredict for both tests observed for pre-JIP version
  Correct trends observed as congestion level is varied, however
  Able to predict within a factor of 2 only 30% of the time
Good performance observed updated model for both cases
  Both near-field and far-field
  Code correctly captures trends as congestion level is varied​
  Predicted within factor of 2 of experimental value 75% of the time
Pre-JIP
Updated

## Slide 16: HySEA homogeneous: results
Clear tendency to overpredict for both tests observed for pre-JIP version
  Correct trends observed as congestion level is varied, however
  Able to predict within a factor of 2 only 30% of the time
Good performance observed updated model for both cases
  Both near-field and far-field
  Code correctly captures trends as congestion level is varied​
  Predicted within factor of 2 of experimental value 75% of the time
Pre-JIP
Updated

## Slide 17: H2 refuelling station mock-up
H2 Refuelling Station mock-up tests published by Shell Global Solutions and HSL in 2006
Experiments included two tests:
    High pressure H2 jet; and
    Pre-mixed stoichiometric H2-Air gas cloud
  Pre-mixed case used as basis for EXSIM validation exercise

## Slide 18: Simulation parameters
Slightly rich H2-air cloud (shown by semi-transparent box)
Ignition location between fuel dispensers (indicated by lightning strike symbol)
Pressures monitored at a range of locations (green cones)
  3 additional monitors underneath mock-up car
Mesh resolution: 436 mm

## Slide 19: Refuelling station: results
Significant underprediction for majority of measurement points observed for pre-JIP version
  Predicted within factor of 2 of experimental value 9% of the time
Updated model observed to significantly overpredict for this case
  Predicted within factor of 2 of experimental value 18% of the time
Investigation into overpredictions ongoing
  May require introduction of turbulence limiter
Pre-JIP
Updated

## Slide 20: Refuelling station: results
Significant underprediction for majority of measurement points observed for pre-JIP version
  Predicted within factor of 2 of experimental value 9% of the time
Updated model observed to significantly overpredict for this case
  Predicted within factor of 2 of experimental value 18% of the time
Investigation into overpredictions ongoing
  May require introduction of turbulence limiter
Pre-JIP
Updated

## Slide 21: Summary
Predictive performance of EXSIM for H2 deflagrations improved as part of multi-year JIP
  Dramatically improved performance over pre-JIP version for H2
Updated model generally performs well across set of modelled cases
  Both in near- and far-field
Further work required to understand and address cause of observed overprediction for refuelling station mock-up case

## Slide 22: SAFEGUARD LIFE, PROPERTY AND THE ENVIRONMENT
bjorn.erling.vembe@dnv.com