## Slide 1: A Novel Tree-Based Hybrid Kernelized Regressor for Predicting Modal Frequencies of Timber Buildings using Weakly Correlated Data
Author: Alireza Entezami, Carmen Amaddeo, Michael Dorn, Maria Pina Limongelli, and Luca Martinelli
2nd Olympiad in Engineering Science – OES 2025

## Slide 2: Importance of SHM in Timber Structures
Timber buildings offer sustainability, lightweight framing, and a high strength-to-weight ratio.
Timber provides environmental benefits such as reduced carbon footprint and renewability.
These structures are sensitive to various environmental parameters such as temperature, humidity, and moisture.
Structural health monitoring (SHM) is a practical process for assessing civil structures under any kind of excitation sources and environmental variability.
SHM enables proactive maintenance by tracking structural responses and environmental conditions, particularly suitable for timber buildings.

## Slide 3: Engineering and Technical Challenges
SHM faces limitations including sensor malfunctions, noise and outliers in measured data, limited accessibility, and difficulty in measurements under harsh environments.
Long-term monitoring, while beneficial, may be costly and often results in incomplete or uncertain datasets.
Although machine learning-aided prediction under the regression problem develops a technical alternative for SHM limitations, predictive models fail in reliable predictions in the presence of incomplete and uncertain datasets.
When the relationships between predictors (environmental parameters) and responses are uncorrelated or weakly correlated, statistical and deep regressors struggle with accuracy and stability due to incomplete training data.

## Slide 4: Proposed Methodology
This research proposes a novel hybrid regression model called Decision Tree Residual-embedded Gaussian Process (DTRGP) to address the engineering and technical challenges.
DTRGP is a two-phase model that combines the strengths of Decision Tree Regression (DTR) and Gaussian Process Regression (GPR).
The proposed regressor aims to predict modal frequencies of timber buildings using some environmental parameters that make weakly correlated relationships with the modal frequencies.

## Slide 5: Proposed Methodology
The proposed regression model leverages a residual learning mechanism to extract hidden environmental patterns, significantly impacting the building modal frequencies.
Residuals from DTR predictions are treated as supplementary environmental features.
These residuals are fused with original environmental data to form an enhanced predictor dataset
The enhanced dataset is used to train GPR in a probabilistic kernel learning framework.

## Slide 6: Application
An 8-story residential timber building in Växjö, Sweden, is selected for validation.
Ambient vibration tests were conducted from Nov 2024 to Apr 2025 to record building acceleration responses from an accelerometer installed in the building floors.
Accelerometers recorded responses on the 3rd, 5th, and 7th floors at 64 Hz.
Operational modal analysis was used to identified three stable vibration modes.
Environmental data (temperature, RH, AH, EMC, wind speed/direction) were collected from a nearby weather station.

## Slide 7
Modal frequencies of the timber building during the short-term monitoring program: (a) mode 1, (b) mode 2, (c) mode 3
Environmental parameters: (a) temperature (⸰C), (b) RH (%), (c) EMC (%), (d) AH (kg/m3), (e) wind speed (m/s), (f) wind direction (⸰)

## Slide 8: Correlation Analysis
All environmental predictors show correlation coefficients < 0.55, indicating weak predictor-response relationships.
Relative Humidity (RH) and Equilibrium Moisture Content (EMC) exhibit moderate positive correlations with Mode 1 (≈ 0.45–0.47).
Temperature shows consistent negative correlations with Mode 1.
Wind speed and direction have very weak or negligible correlations across all modes.
The correlation analysis confirms the challenge of regression modeling under weakly correlated input-output conditions.

## Slide 9: Prediction
Prediction of the building modal frequencies in the testing stage: (a) mode 1, (b) mode 2, (c) mode 3
Prediction of the building modal frequencies in the training stage: (a) mode 1, (b) mode 2, (c) mode 3
R² = 0.9216
R² = 0.9355
R² = 9996
R² = 0.8936
R² = 0.9218
R² = 0.9720

## Slide 10: Conclusions
This study proposes a novel regression model to addresses challenges of limited and weakly correlated SHM data.
Correlation analysis confirms weak correlations between environmental inputs and modal frequencies.
The proposed model, i.e., DTRGP, significantly improves prediction accuracy by obtaining R² values close to one.
This method Demonstrates strong potential for SHM applications with sparse and weakly informative environmental data.

## Slide 11: Thanks for your attention!