## Slide 1: A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
June, 12th, 2025 | Chen Zheng-Han

## Slide 2: Contents
Introduction
Proposed Framework
  2.1 SMOGN technique
  2.2 GRU model
Application: Hardanger Bridge
  3.1 Overview of Hardanger Bridge
  3.2 Predictors
  3.2 Targets
Prediction of Vertical Vibration Responses
  4.1 Prediction Results
  4.2 Comparative Study
Applications
  5.1 Prediction Results
  5.2 Comparative Study
Conclusion

## Slide 3: Introduction
01

## Slide 4
Introduction Existing work
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
AI in SHM
Traditional SHM relies on sensors, but high-cost & complex-installation.
AI/DL methods emerge as alternatives response prediction.
Challenges
Supervised regression models works, but DL methods struggles with small datasets for SHM, causing unstable/biased predictions.
Data Augmentation
Data augmentation techniques enrich training data without new samples, and enhance model robustness
SHM
(Structural Health
Monitoring)
Long-span Bridges
Long-span Bridges face natural (wind-induced vibrations, etc.) & non - natural threats, so SHM matters.

## Slide 5
Introduction This study
Objective
Propose a framework to predict vibration responses under limited data.
Innovation
High accuracy / Small sample conditions / Robustness
Core Idea
SMOGN-GRU Framework
Enhance dataset/ Supervised learning
Workflow
Preprocessing → SMOGN augmentation → GRU prediction → validation
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions

## Slide 6: Proposed Framework
02

## Slide 7
Proposed method Synthetic Minority Over-sampling Technique for Regression with Gaussian Noise (SMOGN)
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Fig. Diagram of SMOGN
Specifically for small-sample regression scenarios, integrating Gaussian noise injection with modified Smote-R.
01
Differentiated sampling strategies, over-sampling for rare samples and under-sampling for standard samples.
02
Adaptively selects interpolation or Gaussian noise to generate synthetic samples based on sample spacing.
03
Features of SMOGN

## Slide 8
Proposed method Gated Recurrent Unit (GRU)
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Advantages of GRU
Easier to implement and understand
Simple Structure
01
2 gating units (40% fewer parameters than LSTM).
Fewer Parameters
03
Lower computational complexity, suitable for large datasets.
Faster Training
02
Two Key Gating Units
Update Gate
1. Determines how much past information to retain
2. Formula:
Reset Gate
1. Controls how much past information to forget
2. Formula:
Hidden State Update
1. Candidate hidden state:
2. Final hidden state:
Core Structure

## Slide 9: Application: Hardanger Bridge
03

## Slide 10
Application Hardanger Bridge: Overview
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Fig. Hardanger Bridge
1
Hardanger Bridge, a 1,380-meter suspension bridge in Norway, longest narrow-span suspension structure when completion
Overview
2
Triaxial accelerometers, ultrasonic anemometers, and GPS sensors. 16 accelerometers on the main girder monitoring vibrations.
SHM System
3
Data from 4 extreme wind events (Ole, Urd, Tor, Nina) in 2015–2016, capturing wind parameters and structural responses.
Dataset

## Slide 11
Application Hardanger Bridge: Predictors and Targets
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Fig. Predictors: Mean wind speed & Mean wind direction
●Mean wind speed and direction ●Angle of attack ●Turbulence intensities ●Standard deviations
●Length scales of the along-wind ●Cross-wind ●Vertical turbulence ●Components and wind gust factor
Predictors
●Vertical vibration acceleration
●Torsional vibration acceleration
Targets

## Slide 12: Prediction of Vertical Vibration Response
04

## Slide 13
01 Data Augmentation
113 sets of data (each containing predictors and targets) are generated via SMOGN.
Before 126 → After 239
Prediction: Vertical Result of SMOGN-GRU
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Interval | Quantity (before SMOGN) | Quantity (after SMOGN)
(0.005, 0.01] | 11 | 29
(0.01, 0.015] | 27 | 48
(0.015, 0.02] | 67 | 102
(0.02, 0.025] | 17 | 52
(0.025, 0.03] | 4 | 8
Total | 126 | 239
Distributions of training sets (before and after SMOGN)
02 Regression
The enhanced training set is used as the input for the GRU model. Residual is used to evaluate the framework.
Fig. Prediction Result

## Slide 14
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Prediction: Vertical Comparative Study
Framework | Training set | Testing set | Whole set
Proposed framework | 0.919 | 0.883 | 0.907
(a) GRU | 0.783 | 0.757 | 0.777
(b) noise injection+GRU | 0.817 | 0.768 | 0.805
(c) SMOGN+SVM | 0.785 | 0.757 | 0.775
(d) SMOGN+MLP | 0.561 | 0.526 | 0.554
value of the proposed framework and four comparative frameworks
The proposed SMOGN-GRU framework shows the best predictive performance with training accuracy 0.919, testing accuracy 0.883, and strong generalization.
Standalone GRU and noise-injection methods have lower testing accuracies (0.757 and 0.768), proving SMOGN's key role in improving robustness.
SMOGN combined with SVM/MLP performs worse (0.757/0.526) than GRU, highlighting GRU's advantage in modeling temporal dependencies.
Findings
Comparative framework
GRU
a
noise injection+GRU
b
SMOGN+SVM
c
S SMOGN+MLP
d

## Slide 15: Prediction of Torsional Vibration Response
05

## Slide 16
01 Data Augmentation
170sets of data (each containing predictors and targets) are generated via SMOGN.
Before 126 → After 196
Prediction: Torsional Result of SMOGN-GRU
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Interval() | Quantity (before SMOGN) | Quantity (after SMOGN)
(2, 6] | 44 | 36
(6, 10] | 64 | 51
(10, 14] | 15 | 89
(14, 18] | 3 | 20
Total | 126 | 196
 | Quantity (before SMOGN) | Quantity (after SMOGN)
(2, 6] | 44 | 36
(6, 10] | 64 | 51
(10, 14] | 15 | 89
(14, 18] | 3 | 20
Total | 126 | 196
Distributions of training sets (before and after SMOGN)
02 Regression
The enhanced training set is used as the input for the GRU model. Residual is used to evaluate the framework.
Fig. Prediction Result

## Slide 17
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions
Prediction: Vertical Comparative Study
Framework | Training set | Testing set | Whole set
Proposed framework | 0.983 | 0.959 | 0.973
(a) GRU | 0.964 | 0.931 | 0.955
(b) noise injection+GRU | 0.911 | 0.869 | 0.893
(c) SMOGN+SVM | 0.885 | 0.808 | 0.868
(d) SMOGN+MLP | 0.713 | 0.657 | 0.702
value of the proposed framework and four comparative frameworks
The proposed SMOGN-GRU framework shows the best predictive performance with training accuracy 0.983, testing accuracy 0.959, and strong generalization.
Standalone GRU and noise-injection methods have lower testing accuracies (0.955 and 0.893), proving SMOGN's key role in improving robustness.
SMOGN combined with SVM/MLP performs worse (0.868/0.702) than GRU, highlighting GRU's advantage in modeling temporal dependencies.
Findings
Comparative framework
GRU
a
noise injection+GRU
b
SMOGN+SVM
c
S SMOGN+MLP
d

## Slide 18: Conclusion
06

## Slide 19
Conclusion
(1) SMOGN augments training data by synthesizing samples from limited SHM records;
(2) The enhanced training set is input into the GRU model to predict wind-induced response.
Proposed SMOGN-GRU method
The proposed SMOGN-GRU framework article has high accuracy in predicting two types of wind vibration responses.
Resolves small-sample limitations in bridge vibration prediction
Shows practical value for high-cost SHM systems in extreme wind scenarios.
Key findings
A Novel Data-Augmented Deep Learning Framework for Predicting Wind-Induced Vibrations in Long-Span Bridges under Small Sample Conditions

## Slide 20: Thank you for your attention.
Chen Zheng-Han