## Slide 1: Dynamic Monitoring of Bridge Structures under Seasonal Temperature Variability by Reconstruction Error-based Density Clustering for Anomaly Detection
Author: Mohammad Omidi1,2, Alireza Entezami2, Alberto Corigliano2
2nd Olympiad in Engineering Science – OES 2025
1 Department of Thermal and Fluid Engineering, University of Twente, Netherlands
2 Department of civil and environmental engineering, Politecnico di Milano, Milan, Italy

## Slide 2: Motivation and Problem Statement
Ensuring safety of bridges under variable environmental & operational conditions is critical.
Modal frequencies: sensitive indicators of structural change.
Main challenge: Distinguishing real structural anomalies from environmental effects (e.g., seasonal temperature variations).
Traditional damage detection faces issues:
  False alarms (unnecessary interventions)
  Missed detections (safety risk)

## Slide 3: Existing Methods
Traditional SHM Approaches:
  Physics-based: struggle under environmental variability.
  Data-driven: often require thresholds, are sensitive to noise.
Unsupervised Learning:
  Needs robust, threshold-free techniques.
  Single model approaches miss complex patterns.
Goal: Achieve robust anomaly detection, minimizing both false alarms and missed detections.

## Slide 4: Proposed Solution – REDCAN Framework
Reconstruction Error-based Density Clustering for Anomaly Detection
Combines deep autoencoder with DBSCAN clustering.
Two main stages:
  Feature Normalization: Autoencoder reconstructs modal frequencies, errors highlight deviations.
  Clustering: DBSCAN clusters errors, separating normal from anomalous states.

## Slide 5: Deep Autoencoder – Feature Normalization
Unsupervised neural networks learns compressed data representation.
Trained to reconstruct normal modal frequency behavior.
Output: Reconstruction error for each data point (measures deviation).

## Slide 6: Density-Based Clustering (DBSCAN)
DBSCAN clusters data based on local density, not distance to center.
Auto-tuned into two clusters:
  Normal (label 1)
  Anomaly/Damage (label -1)
No need for preset thresholds or number of clusters.
Noise in reconstruction error → detected anomaly.

## Slide 7: Experimental Validation – Z24 Bridge
Z24 bridge (Switzerland): benchmark for SHM validation.

## Slide 8: Experimental Validation – Z24 Bridge
Dataset: Long-term modal frequencies under varying temperature and known damage events.
Key Environmental Factor: Temperature (esp. freezing events → frequency spikes).

## Slide 9: Results: Reconstruction Errors
Modal frequencies affected by temperature (sharp spikes during freezing events).
Autoencoder reduces temperature effect, but outliers (due to anomalies or large temp changes) persist as reconstruction errors.

## Slide 10: Results: Effective Anomaly Detection
DBSCAN on reconstruction errors:
  Separates normal from anomalous/damaged states.
  Achieves very low false alarm rate (<0.1%).
  Accurately identifies damage, even under environmental variability.

## Slide 11: Conclusions
REDCAN achieves highly accurate, robust anomaly detection for bridges.
Outperforms traditional and single-model approaches under challenging environmental conditions.
Threshold-free, robust to severe environmental variability.
Binary classification: simple label interpretation.
REDCAN provides a powerful, automated, and reliable tool for real-world bridge health monitoring—effectively separating damage from environmental noise and paving the way for smarter, safer infrastructure management.

## Slide 12: Thanks for your attention!