## Slide 1: A Fully Customized Vehicle Scanning System: Field Trials on Two Large-Scale Bridges
M. Alamdari1, A. Calderon Hurtado1, J. Xu1, D. Dias-da-Costa2, R. Salleh3
1 School of Civil and Environmental Engineering, University of New South Wales, Sydney, NSW 2052, Australia
2 School of Civil Engineering, The University of Sydney, NSW 2006, Australia
3 School of Computer Science and Engineering, University of New South Wales, Sydney, NSW 2052, Australia m.makkialamdari@unsw.edu.au

## Slide 2: Vehicle Scanning Method (iSHM, drive-by bridge inspection)

## Slide 3: Drive-by Bridge Inspection
Fujino, Y., & Siringoringo, D. M. (2011). Bridge monitoring in Japan: the needs and strategies. Structure and Infrastructure Engineering, 7(7-8), 597-611.
Malekjafarian, A., McGetrick, P.J. and OBrien, E.J., 2015. A review of indirect bridge monitoring using passing vehicles. Shock and vibration, 2015(1), p.286139.
[1]
[2]
Drive by bridge inspection can potentially offer:
A scalable bridge monitoring solution
A more cost-effective approach
No need for power and data transmission access onsite
Removes the burden of ongoing system maintenance and sensor replacement with conventional SHM

## Slide 4: Vehicle-Bridge Interaction (VBI):
Alamdari, M.M., 2024. An evolutionary vehicle scanning method for bridges based on time series segmentation and change point detection. Mechanical Systems and Signal Processing, 210, p.111173.

## Slide 5: Change Point Detection

## Slide 6: Matrix Profile
An all-subsequences set
:
A subsequence with length
The z-normalized Euclidean distance
Alamdari, M.M., 2024. An evolutionary vehicle scanning method for bridges based on time series segmentation and change point detection. Mechanical Systems and Signal Processing, 210, p.111173.

## Slide 7: MP: Motif Discovery

## Slide 8: MP: Anomaly Detection

## Slide 9: Change Point Detection

## Slide 10: Change Point Detection

## Slide 11: Bridge Inspection Vehicle Set-up, Direct and Indirect Sensing

## Slide 12: Inspection Vehicle
Vehicle Speed: [0.1 – 10] m/s
M: 20 Kg
L= 80 cm

## Slide 13: Inspection Vehicle
Acceleration response from the accelerometer mounted on the front-right suspension arm
Vehicle Speed: 0.17 m/s
Sampling Frequency: 1600 Hz

## Slide 14: Target Bridge (I)
Pedestrian bridge at UNSW campus
Simply Supported Steel Bridge
17m length
~ 1m width

## Slide 15: Direct Sensing
¼ of the span
¾ of the span
Mid-span

## Slide 16
Direct Sensing

## Slide 17
Indirect Sensing
Illustration of acceleration time series from indirect sensing,
  front-right axle,
  front-left axle,
  rear-right axle,
  rear-left axle.

## Slide 18
Indirect Sensing

## Slide 19: CAC Under Nominal Bridge State

## Slide 20: CAC Under Changed State

## Slide 21: Target Bridge (II)
Bulli Colliery Bridge
A steel girder bridge
span is 23.9 m

## Slide 22: Direct Sensing
¼ of the span
¾ of the span
Mid-span

## Slide 23
Direct Sensing

## Slide 24
Indirect Sensing
Illustration of acceleration time series from indirect sensing,
  front-right axle,
  front-left axle,
  rear-right axle,
  rear-left axle.

## Slide 25
Indirect Sensing

## Slide 26: CAC Under Nominal Bridge State

## Slide 27: Conclusions
A customised inspection vehicle was designed and tested for drive by bridge scanning.
The potential of iSHM to extract bridge fundamental frequency was shown on two large-scale bridges.
The extracted features from the acceleration response of the vehicle have the potential to be used for structural integrity assessment.
The effect of long-term trends, as well as environmental and operational variations, should be studied.
The framework should be tested on different types of bridge structures.
Future Works

## Slide 28: Publications
Tyler, G., Luo, S., Hurtado, A.C. and Alamdari, M.M., 2025. Semi-supervised bridge indirect structural health monitoring using Isolation Distributional Kernels. Mechanical Systems and Signal Processing, 226, p.112296.
Alamdari, M.M., 2024. An evolutionary vehicle scanning method for bridges based on time series segmentation and change point detection. Mechanical Systems and Signal Processing, 210, p.111173.
Hurtado, A.C., Alamdari, M.M., Atroshchenko, E., Chang, K.C. and Kim, C.W., 2024. A data-driven methodology for bridge indirect health monitoring using unsupervised computer vision. Mechanical Systems and Signal Processing, 210, p.111109.
Hurtado, A.C., Kaur, K., Alamdari, M.M., Atroshchenko, E., Chang, K.C. and Kim, C.W., 2023. Unsupervised learning-based framework for indirect structural health monitoring using adversarial autoencoder. Journal of Sound and Vibration, 550, p.117598.
Cheema, P., Alamdari, M.M., Vio, G., Azizi, L. and Luo, S., 2023. On the use of matrix profiles and optimal transport theory for multivariate time series anomaly detection within structural health monitoring. Mechanical Systems and Signal Processing, 204, p.110797.
Cheema, P., Alamdari, M.M., Chang, K.C., Kim, C.W. and Sugiyama, M., 2022. A drive-by bridge inspection framework using non-parametric clusters over projected data manifolds. Mechanical Systems and Signal Processing, 180, p.109401.
Alamdari, M.M., Chang, K.C., Kim, C.W., Kildashti, K. and Kalhori, H., 2021. Transmissibility performance assessment for drive-by bridge inspection. Engineering Structures, 242, p.112485.
Kildashti, K., Alamdari, M.M., Kim, C.W., Gao, W. and Samali, B., 2020. Drive-by-bridge inspection for damage identification in a cable-stayed bridge: Numerical investigations. Engineering structures, 223, p.110891.
Google Scholar

## Slide 29: Sponsors

## Slide 30
m.makkialamdari@unsw.edu.au