## Slide 1: Hybrid Clustering-Based Anomaly Detection for Damage Detection in Civil Structures Subjected to Environmental Changes
Author: Mohammad Omidi1,2, Alireza Entezami2, Alberto Corigliano2
2nd Olympiad in Engineering Science – OES 2025
1 Department of Thermal and Fluid Engineering, University of Twente, Netherlands
2 Department of civil and environmental engineering, Politecnico di Milano, Milan, Italy

## Slide 2: Motivation and Problem Statement
Ensuring safety of bridges under variable environmental & operational conditions is critical.
Modal frequencies: sensitive indicators of structural change.
Main challenge: Distinguishing real structural anomalies from environmental effects (e.g., seasonal temperature variations).
Traditional damage detection faces issues:
  False alarms (unnecessary interventions)
  Missed detections (safety risk)

## Slide 3: Existing Methods
Traditional SHM Approaches:
  Physics-based: struggle under environmental variability.
  Data-driven: often require thresholds, are sensitive to noise.
Unsupervised Learning:
  Needs robust, threshold-free techniques.
  Single model approaches miss complex patterns.
Goal: Achieve robust anomaly detection, minimizing both false alarms and missed detections.

## Slide 4: Methodology – HCAD
Hybrid Clustering-Based Anomaly Detection (HCAD):
Stage 1: Gaussian Mixture Model (GMM) for initial probabilistic clustering.
Stage 2: K-means Clustering (KMC) initialized with GMM centroids for refined clustering.
Stage 3: Damage Indicator, Clustering-aided Damage Indicator (CDI) quantifies deviation from centroids.
Stage 4: Thresholding, Generalized Extreme Value (GEV) model distinguishes anomalies
Data
GMM
KMC
CDI
GEV Threshold
Damage detection

## Slide 5: GMM-Based Pre-Clustering
Key Steps:
Assigns membership probabilities to each data point.
Parameters estimated via Expectation-Maximization (EM) algorithm.
Gap statistic used to determine optimal number of clusters

## Slide 6: KMC-Enhanced Clustering
K-means Clustering:
Uses GMM-derived centroids as initialization points.
Refines clusters by minimizing intra-cluster variance.
Avoids random initialization and additional heuristics for cluster number

## Slide 7: Clustering-Aided Damage Indicator (CDI)
CDI Calculation:
Measures Euclidean distance from each sample to its closest KMC centroid.
Training Phase: CDI values used to fit a GEV-based threshold.
Testing Phase: New samples exceeding threshold flagged as anomalies (potential damage)

## Slide 8: Experimental Validation – Z24 Bridge
Z24 bridge (Switzerland): benchmark for SHM validation.
Three-span concrete bridge monitored over a year.

## Slide 9: Experimental Validation – Z24 Bridge
Dataset: Long-term modal frequencies under varying temperature and known damage events.
Key Environmental Factor: Temperature (esp. freezing events → frequency spikes).

## Slide 10: Process
Stage | Method
Data Collection | Vibration monitoring
Data Split | 75% of NC training
Feature Extraction | Modal frequencies
Cluster Selection | Gap statistic
GMM Pre-Clustering | Soft clustering
Enhanced KMC | Clustering based GMM
CDI Calculation | Euclidean distance
Threshold Estimation | GEV model, 36 blocks
Anomaly Detection | CDI vs threshold

## Slide 11: Results
Normal Condition (NC):
Training samples (blue): All CDI values are below the threshold, indicating correct classification of normal states.
Testing samples (green): Most CDI values remain below the threshold; only 6 samples exceed, resulting in a false positive rate of 0.18%.
Damaged Condition (DC):
Testing samples (red): Most CDI values are above the threshold, correctly indicating damage.
21 damaged samples fall below the threshold, leading to a false negative

## Slide 12: Conclusions
HCAD Advantages:
  Robust to environmental variability.
  Efficient and unsupervised—no need for labeled damage data.
  High accuracy and low error rates in real-world validation.
Impact: Enhances reliability of vibration-based SHM for civil infrastructure

## Slide 13: Thanks for your attention!